## Slide 1: JLR VPD EDS Heating Element (FY 2025-26)
10-Sept-2025

## Slide 2: Change history
Issue | Description | Date | Owner
01 | New Document | 31-12-2025 | Vyshak PV / Moinkhan S/ Akash H

## Slide 3: Concept
ICE ACCUMULATION CONCERN
REQUIREMENT
Radome image to understand Snow Accumulation Concern
1. Due to inward profile of grille leap at ADAS area there are chances of snow accumulation, due to which efficiency of radar might get reduced.
2. Snow accumulation assumptions highlighted in yellow colour.
Requirement :- to introduce new part heating element to melt snow.
Constraints:- packaging seems very close with current position (refer next slide) of ADAS and radar bracket (screenshot highlighted next slide).

## Slide 4: Concept
INITIAL PROPOSAL GIVEN TO AVOID TOOL COST
Initial Proposal can be shared with Design Team ::
Profile created outward to avoid Snow accumulation to improve ADAS efficiency.
PROPOSED GRILLE SURFACE
EXISTING GRILLE SURFACE
Heating Element need to be incorporated at the radome area If the style modification proposal is not so feasible considering the theme ,
ADAS Unit
ADAS BRACKET
LOWER GRILLE
FINISHERS
ADAS FOV
BUMPER SKIN
Bumper Beam

## Slide 5: Heating element :: Packaging Requirements
Heating Wires shall run vertical in carline inside the Field of View
ensure Field of View accounts for radar positional tolerance
Heating Wires shall remain vertical for at least A = 1mm outside of the Field of View
The edge of the foil shall be a minimum of B = 2mm outside of the heating wires
Edge of the carrier to any other mating part feature (e.g. hole, rib, screw boss) shall have a clearance of 1mm within the assembly
The min distance between foil edge & Carrier edge ie C=1.4mm
Foil shall be away from any parting line by at least 0.5mm for parts over 800mm this value has to be confirmed with supplier
Total thickness of the Carrier and Mating part shall be reviewed for radar attenuation mitigation.
Section A-A
A
A
Radome Area
Heating Element
ADAS Unit

## Slide 6: Heating element :: Packaging Requirements / reference
Mounting Snap :: 7 Nos.
Locators :: 2 Nos.
Locating & mounting scheme is highlighted in image from reference program.
It’s recommended to use snap mounting for the serviceability.
Ref. EI_V8EM-17K945-AA--L460 SV 28 MY FR BMPRLWG GRL
Mounting Snap
Radome Cover
FR LWR GRL

## Slide 7: Heating element :: Packaging Requirements
A 0,5mm GAP is required between the grille and the carrier as shown in section as per supplier input. :: It’s need to be approved from JLR design team & DVA
A
A
Section A-A
Thickness Consideration ::
  Part thickness is 5.8mm
  (Radome Aesthetical Portion 3.1mm thk
  + Radome Technical Portion 2.7mm thk )
Material Consideration ::
  PC+ABS
5.8mm

## Slide 8: Heating element :: Packaging Requirements / reference
ADAS Unit
LOWER GRILLE
ADAS FOV
ADAS BRACKET
Radome Cover

## Slide 9: Assembly Flight Path:
ADAS unit assembly flight path:
ADAS unit will mount on ADAS bracket.
Heating Element gets In molded with Radome Cover. :: will be fitted from front side of LWR GRL
ADAS and ADAS Bracket will mount on Lower Grille in X :: will be fitted from back side of LWR GRL
LOWER GRILLE
ADAS Unit
Radome Cover + Heating Element
ADAS MTG Bracker
FR Camera

## Slide 10: Heating element :: Manufacturing Process
COPPER WIRES
Heating element copper wire is shown in image for reference.
This portion of Radome Cover will be formed in the 1st stage of 2K-Injection moulding process
REFER NEXT SLIDE
CONNECTOR PORT
FOIL

## Slide 11: Heating element :: Moulding Process
Heating Element
(Copper Wire + Foil) will be placed in cavity
Radome Cover Part
Will be snapped on LWR Grill
Here it’s a combination of Over Moulding & 2K Moulding to keep the heating element in the middle of Radome Cover
STAGE :: 1 (Over Moulding + 2K 1st Half)
Radome Cover_MTG/Technical Portion
Material :: PC+ABS
Heating Element will be over moulded in the 2K moulding 1st stage.
STAGE :: 2 (2K Moulding 2nd Half)
Radome Cover_Aesthetical/style Portion
Material :: PC+ABS
will be moulded in the 2K moulding 2nd stage.

## Slide 12: 2K Moulding Process :: Reference
180Deg Rotating Core Half
1St Moulding Cavity
2nd Moulding Cavity